## Slide 1
Chapter 5 Link Layer and LANs
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) in substantially unaltered form, that you mention their source (after all, we’d like people to use our book!)
If you post any slides in substantially unaltered form on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2007
J.F Kurose and K.W. Ross, All Rights Reserved
Computer Networking: A Top Down Approach 4th edition. Jim Kurose, Keith Ross Addison-Wesley, July 2007.

## Slide 2: Chapter 5: The Data Link Layer
Our goals:
understand principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  reliable data transfer, flow control: done!
instantiation and implementation of various link layer technologies

## Slide 3: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-layer Addressing
5.5 Ethernet
5.6 Link-layer switches
5.7 PPP
5.8 Link virtualization: ATM, MPLS

## Slide 4: Link Layer: Introduction
Some terminology:
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
layer-2 packet is a frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to adjacent node over a link

## Slide 5: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide rdt over link
transportation analogy
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 6: Link Layer Services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, dest
    different from IP address!
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 7: Link Layer Services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 8: Where is the link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC)
  Ethernet card, PCMCI card, 802.11 card
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
host schematic
application
transport
network
link
link
physical

## Slide 9: Adaptors Communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 10: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-layer Addressing
5.5 Ethernet
5.6 Link-layer switches
5.7 PPP
5.8 Link Virtualization: ATM. MPLS

## Slide 11: Error Detection
EDC= Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
otherwise

## Slide 12: Parity Checking
Single Bit Parity:
Detect single bit errors
Two Dimensional Bit Parity:
Detect and correct single bit errors
0
0

## Slide 13: Internet checksum (review)
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless?
Goal: detect “errors” (e.g., flipped bits) in transmitted packet (note: used at transport layer only)

## Slide 14: Checksumming: Cyclic Redundancy Check
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (Ethernet, 802.11 WiFi, ATM)

## Slide 15: CRC Example
Want:
  D.2r XOR R = nG
equivalently:
  D.2r = nG XOR R
equivalently:
if we divide D.2r by G, want remainder R
R = remainder[ ]
D.2r
G

## Slide 16: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-layer Addressing
5.5 Ethernet
5.6 Link-layer switches
5.7 PPP
5.8 Link Virtualization: ATM, MPLS

## Slide 17: Multiple Access Links and Protocols
Two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch and host
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 18: Multiple Access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination

## Slide 19: Ideal Multiple Access Protocol
Broadcast channel of rate R bps
1. when one node wants to transmit, it can send at rate R.
2. when M nodes want to transmit, each can send at average rate R/M
3. fully decentralized:
  no special node to coordinate transmissions
  no synchronization of clocks, slots
4. simple

## Slide 20: MAC Protocols: a taxonomy
Three broad classes:
Channel Partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
Random Access
  channel not divided, allow collisions
  “recover” from collisions
“Taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 21: Channel Partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = pkt trans time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have pkt, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame

## Slide 22: Channel Partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have pkt, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 23: Random Access Protocols
When node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
Examples of random access MAC protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 24: Slotted ALOHA
Assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
Operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with prob. p until success

## Slide 25: Slotted ALOHA
Pros
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization

## Slide 26: Slotted Aloha efficiency
suppose: N nodes with many frames to send, each transmits in slot with probability p
prob that given node has success in a slot = p(1-p)N-1
prob that any node has a success = Np(1-p)N-1
max efficiency: find p* that maximizes Np(1-p)N-1
for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
Max efficiency = 1/e = .37
Efficiency : long-run fraction of successful slots (many nodes, all with many frames to send)
At best: channel
used for useful
transmissions 37%
of time!
!

## Slide 27: Pure (unslotted) ALOHA
unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 28: Pure Aloha efficiency
P(success by given node) = P(node transmits) .
P(no other node transmits in [p0-1,p0] .
P(no other node transmits in [p0-1,p0]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n -> infty ...
= 1/(2e) = .18
even worse than slotted Aloha!

## Slide 29: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit:
If channel sensed idle: transmit entire frame
If channel sensed busy, defer transmission
human analogy: don’t interrupt others!

## Slide 30: CSMA collisions
collisions can still occur:
propagation delay means
two nodes may not hear
each other’s transmission
collision:
entire packet transmission
time wasted
spatial layout of nodes
note:
role of distance & propagation delay in determining collision probability

## Slide 31: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength
human analogy: the polite conversationalist

## Slide 32: CSMA/CD collision detection

## Slide 33: “Taking Turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
Random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 34: “Taking Turns” MAC protocols
Polling:
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices
concerns:
  polling overhead
  latency
  single point of failure (master)
master
slaves
poll
data
data

## Slide 35: “Taking Turns” MAC protocols
Token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)
T
data
(nothing
to send)
T

## Slide 36: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, IBM Token Ring

## Slide 37: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Link-layer switches
5.7 PPP
5.8 Link Virtualization: ATM, MPLS

## Slide 38: MAC Addresses and ARP
32-bit IP address:
  network-layer address
  used to get datagram to destination IP subnet
MAC (or LAN or physical or Ethernet) address:
  function: get frame from one interface to another physically-connected interface (same network)
  48 bit MAC address (for most LANs)
    burned in NIC ROM, also sometimes software settable

## Slide 39: LAN Addresses and ARP
Each adapter on LAN has unique LAN address
Broadcast address =
FF-FF-FF-FF-FF-FF
= adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 40: LAN Address (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
(a) MAC address: like Social Security Number
(b) IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address NOT portable
  address depends on IP subnet to which node is attached

## Slide 41: ARP: Address Resolution Protocol
Each IP node (host, router) on LAN has ARP table
ARP table: IP/MAC address mappings for some LAN nodes
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
MAC address of B
knowing B’s IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 42: ARP protocol: Same LAN (network)
A wants to send datagram to B, and B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  dest MAC address = FF-FF-FF-FF-FF-FF
  all machines on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 43: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
A
74-29-9C-E8-FF-55
222.222.222.221
88-B2-2F-54-1A-0F
B
222.222.222.222
49-BD-D2-C7-56-2A
walkthrough: send datagram from A to B via R
assume A knows B’s IP address
two ARP tables in router R, one for each IP network (LAN)

## Slide 44
A creates IP datagram with source A, destination B
A uses ARP to get R’s MAC address for 111.111.111.110
A creates link-layer frame with R's MAC address as dest, frame contains A-to-B IP datagram
A’s NIC sends frame
R’s NIC receives frame
R removes IP datagram from Ethernet frame, sees its destined to B
R uses ARP to get B’s MAC address
R creates frame containing A-to-B IP datagram sends to B
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
A
74-29-9C-E8-FF-55
222.222.222.221
88-B2-2F-54-1A-0F
B
222.222.222.222
49-BD-D2-C7-56-2A
This is a really important
example – make sure you
understand!

## Slide 45: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Link-layer switches
5.7 PPP
5.8 Link Virtualization: ATM and MPLS

## Slide 46: Ethernet
“dominant” wired LAN technology:
cheap $20 for NIC
first widely used LAN technology
simpler, cheaper than token LANs and ATM
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet
sketch

## Slide 47: Star topology
bus topology popular through mid 90s
  all nodes in same collision domain (can collide with each other)
today: star topology prevails
  active switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
switch
bus: coaxial cable
star

## Slide 48: Ethernet Frame Structure
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
Preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates

## Slide 49: Ethernet Frame Structure (more)
Addresses: 6 bytes
  if adapter receives frame with matching destination address, or with broadcast address (eg ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
Type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: checked at receiver, if error is detected, frame is dropped

## Slide 50: Ethernet: Unreliable, connectionless
connectionless: No handshaking between sending and receiving NICs
unreliable: receiving NIC doesn’t send acks or nacks to sending NIC
  stream of datagrams passed to network layer can have gaps (missing datagrams)
  gaps will be filled if app is using TCP
  otherwise, app will see gaps
Ethernet’s MAC protocol: unslotted CSMA/CD

## Slide 51: Ethernet CSMA/CD algorithm
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission If NIC senses channel busy, waits until channel idle, then transmits
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters exponential backoff: after mth collision, NIC chooses K at random from {0,1,2,…,2m-1}. NIC waits K·512 bit times, returns to Step 2

## Slide 52: Ethernet’s CSMA/CD (more)
Jam Signal: make sure all other transmitters are aware of collision; 48 bits
Bit time: .1 microsec for 10 Mbps Ethernet ; for K=1023, wait time is about 50 msec
Exponential Backoff:
Goal: adapt retransmission attempts to estimated current load
  heavy load: random wait will be longer
first collision: choose K from {0,1}; delay is K· 512 bit transmission times
after second collision: choose K from {0,1,2,3}…
after ten collisions, choose K from {0,1,2,3,4,…,1023}
See/interact with Java
applet on AWL Web site:
highly recommended !

## Slide 53: CSMA/CD efficiency
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!

## Slide 54: 802.3 Ethernet Standards: Link & Physical Layers
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10G bps
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister
pair) physical layer

## Slide 55: Manchester encoding
used in 10BaseT
each bit has a transition
allows clocks in sending and receiving nodes to synchronize to each other
  no need for a centralized, global clock among nodes!
Hey, this is physical-layer stuff!

## Slide 56: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3 Multiple access protocols
5.4 Link-layer Addressing
5.5 Ethernet
5.6 Link-layer switches
5.7 PPP
5.8 Link Virtualization: ATM, MPLS

## Slide 57: Hubs
… physical-layer (“dumb”) repeaters:
  bits coming in one link go out all other links at same rate
  all nodes connected to hub can collide with one another
  no frame buffering
  no CSMA/CD at hub: host NICs detect collisions
twisted pair
hub

## Slide 58: Switch
link-layer device: smarter than hubs, take active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 59: Switch: allows multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ simultaneously, without collisions
  not possible with dumb hub
A
A’
B
B’
C
C’
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 60: Switch Table
Q: how does switch know that A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?
A
A’
B
B’
C
C’
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 61: Switch: self-learning
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 62: Switch: frame filtering/forwarding
When frame received:
1. record link associated with sending host
2. index switch table using MAC dest address
3. if entry found for destination then {
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 63: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination unknown:
flood
A’ A
destination A location known:
A’
4
60
selective send

## Slide 64: Interconnecting switches
switches can be connected together
A
B
Q: sending from A to G - how does S1 know to forward frame destined to F via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 65: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
1
2

## Slide 66: Institutional network
to external
network
router
IP subnet
mail server
web server

## Slide 67: Switches vs. Routers
both store-and-forward devices
  routers: network layer devices (examine network layer headers)
  switches are link layer devices
routers maintain routing tables, implement routing algorithms
switches maintain switch tables, implement filtering, learning algorithms

## Slide 68: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Hubs and switches
5.7 PPP
5.8 Link Virtualization: ATM

## Slide 69: Point to Point Data Link Control
one sender, one receiver, one link: easier than broadcast link:
  no Media Access Control
  no need for explicit MAC addressing
  e.g., dialup link, ISDN line
popular point-to-point DLC protocols:
  PPP (point-to-point protocol)
  HDLC: High level data link control (Data link used to be considered “high layer” in protocol stack!

## Slide 70: PPP Design Requirements [RFC 1557]
packet framing: encapsulation of network-layer datagram in data link frame
  carry network layer data of any network layer protocol (not just IP) at same time
  ability to demultiplex upwards
bit transparency: must carry any bit pattern in the data field
error detection (no correction)
connection liveness: detect, signal link failure to network layer
network layer address negotiation: endpoint can learn/configure each other’s network address

## Slide 71: PPP non-requirements
no error correction/recovery
no flow control
out of order delivery OK
no need to support multipoint links (e.g., polling)
Error recovery, flow control, data re-ordering
all relegated to higher layers!

## Slide 72: PPP Data Frame
Flag: delimiter (framing)
Address: does nothing (only one option)
Control: does nothing; in the future possible multiple control fields
Protocol: upper layer protocol to which frame delivered (eg, PPP-LCP, IP, IPCP, etc)

## Slide 73: PPP Data Frame
info: upper layer data being carried
check: cyclic redundancy check for error detection

## Slide 74: Byte Stuffing
“data transparency” requirement: data field must be allowed to include flag pattern <01111110>
  Q: is received <01111110> data or flag?
Sender: adds (“stuffs”) extra < 01111110> byte after each < 01111110> data byte
Receiver:
  two 01111110 bytes in a row: discard first byte, continue data reception
  single 01111110: flag byte

## Slide 75: Byte Stuffing
flag byte
pattern
in data
to send
flag byte pattern plus
stuffed byte in transmitted data

## Slide 76: PPP Data Control Protocol
Before exchanging network-layer data, data link peers must
configure PPP link (max. frame length, authentication)
learn/configure network
layer information
  for IP: carry IP Control Protocol (IPCP) msgs (protocol field: 8021) to configure/learn IP address

## Slide 77: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Hubs and switches
5.7 PPP
5.8 Link Virtualization: ATM and MPLS

## Slide 78: Virtualization of networks
Virtualization of resources: powerful abstraction in systems engineering:
computing examples: virtual memory, virtual devices
  Virtual machines: e.g., java
  IBM VM os from 1960’s/70’s
layering of abstractions: don’t sweat the details of the lower layer, only deal with lower layers abstractly

## Slide 79: The Internet: virtualizing networks
1974: multiple unconnected nets
  ARPAnet
  data-over-cable networks
  packet satellite network (Aloha)
  packet radio network
… differing in:
  addressing conventions
  packet formats
  error recovery
  routing
ARPAnet
satellite net
"A Protocol for Packet Network Intercommunication",
V. Cerf, R. Kahn, IEEE Transactions on Communications,
May, 1974, pp. 637-648.

## Slide 80: The Internet: virtualizing networks
ARPAnet
satellite net
gateway
Internetwork layer (IP):
addressing: internetwork appears as single, uniform entity, despite underlying local network heterogeneity
network of networks
Gateway:
“embed internetwork packets in local packet format or extract them”
route (at internetwork level) to next gateway

## Slide 81: Cerf & Kahn’s Internetwork Architecture
What is virtualized?
two layers of addressing: internetwork and local network
new layer (IP) makes everything homogeneous at internetwork layer
underlying local network technology
  cable
  satellite
  56K telephone modem
  today: ATM, MPLS
… “invisible” at internetwork layer. Looks like a link layer technology to IP!

## Slide 82: ATM and MPLS
ATM, MPLS separate networks in their own right
  different service models, addressing, routing from Internet
viewed by Internet as logical link connecting IP routers
  just like dialup link is really part of separate network (telephone network)
ATM, MPLS: of technical interest in their own right

## Slide 83: Asynchronous Transfer Mode: ATM
1990’s/00 standard for high-speed (155Mbps to 622 Mbps and higher) Broadband Integrated Service Digital Network architecture
Goal: integrated, end-end transport of carry voice, video, data
  meeting timing/QoS requirements of voice, video (versus Internet best-effort model)
  “next generation” telephony: technical roots in telephone world
  packet-switching (fixed length packets, called “cells”) using virtual circuits

## Slide 84: ATM architecture
adaptation layer: only at edge of ATM network
  data segmentation/reassembly
  roughly analagous to Internet transport layer
ATM layer: “network” layer
  cell switching, routing
physical layer
physical
ATM
AAL
physical
ATM
AAL
physical
ATM
physical
ATM
end system
end system
switch
switch

## Slide 85: ATM: network or link layer?
Vision: end-to-end transport: “ATM from desktop to desktop”
  ATM is a network technology
Reality: used to connect IP backbone routers
  “IP over ATM”
  ATM as switched link layer, connecting IP routers
ATM
network
IP
network

## Slide 86: ATM Adaptation Layer (AAL)
ATM Adaptation Layer (AAL): “adapts” upper layers (IP or native ATM applications) to ATM layer below
AAL present only in end systems, not in switches
AAL layer segment (header/trailer fields, data) fragmented across multiple ATM cells
  analogy: TCP segment in many IP packets
physical
ATM
AAL
physical
ATM
AAL
physical
ATM
physical
ATM
end system
end system
switch
switch

## Slide 87: ATM Adaptation Layer (AAL) [more]
Different versions of AAL layers, depending on ATM service class:
AAL1: for CBR (Constant Bit Rate) services, e.g. circuit emulation
AAL2: for VBR (Variable Bit Rate) services, e.g., MPEG video
AAL5: for data (eg, IP datagrams)
AAL PDU
ATM cell
User data

## Slide 88: ATM Layer
Service: transport cells across ATM network
analogous to IP network layer
very different services than IP network layer
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 89: ATM Layer: Virtual Circuits
VC transport: cells carried on VC from source to dest
  call setup, teardown for each call before data can flow
  each packet carries VC identifier (not destination ID)
  every switch on source-dest path maintain “state” for each passing connection
  link,switch resources (bandwidth, buffers) may be allocated to VC: to get circuit-like perf.
Permanent VCs (PVCs)
  long lasting connections
  typically: “permanent” route between to IP routers
Switched VCs (SVC):
  dynamically set up on per-call basis

## Slide 90: ATM VCs
Advantages of ATM VC approach:
  QoS performance guarantee for connection mapped to VC (bandwidth, delay, delay jitter)
Drawbacks of ATM VC approach:
  Inefficient support of datagram traffic
  one PVC between each source/dest pair) does not scale (N*2 connections needed)
  SVC introduces call setup latency, processing overhead for short lived connections

## Slide 91: ATM Layer: ATM cell
5-byte ATM cell header
48-byte payload
  Why?: small payload -> short cell-creation delay for digitized voice
  halfway between 32 and 64 (compromise!)
Cell header
Cell format

## Slide 92: ATM cell header
VCI: virtual channel ID
  will change from link to link thru net
PT: Payload type (e.g. RM cell versus data cell)
CLP: Cell Loss Priority bit
  CLP = 1 implies low priority cell, can be discarded if congestion
HEC: Header Error Checksum
  cyclic redundancy check

## Slide 93: ATM Physical Layer (more)
Two pieces (sublayers) of physical layer:
Transmission Convergence Sublayer (TCS): adapts ATM layer above to PMD sublayer below
Physical Medium Dependent: depends on physical medium being used
TCS Functions:
  Header checksum generation: 8 bits CRC
  Cell delineation
  With “unstructured” PMD sublayer, transmission of idle cells when no data cells to send

## Slide 94: ATM Physical Layer
Physical Medium Dependent (PMD) sublayer
SONET/SDH: transmission frame structure (like a container carrying bits);
  bit synchronization;
  bandwidth partitions (TDM);
  several speeds: OC3 = 155.52 Mbps; OC12 = 622.08 Mbps; OC48 = 2.45 Gbps, OC192 = 9.6 Gbps
TI/T3: transmission frame structure (old telephone hierarchy): 1.5 Mbps/ 45 Mbps
unstructured: just cells (busy/idle)

## Slide 95: IP-Over-ATM
Classic IP only
3 “networks” (e.g., LAN segments)
MAC (802.3) and IP addresses
IP over ATM
replace “network” (e.g., LAN segment) with ATM network
ATM addresses, IP addresses
ATM
network
Ethernet
LANs
Ethernet
LANs

## Slide 96: IP-Over-ATM
AAL
ATM
phy
phy
Eth
IP
ATM
phy
ATM
phy
app
transport
IP
AAL
ATM
phy
app
transport
IP
Eth
phy

## Slide 97: Datagram Journey in IP-over-ATM Network
at Source Host:
  IP layer maps between IP, ATM dest address (using ARP)
  passes datagram to AAL5
  AAL5 encapsulates data, segments cells, passes to ATM layer
ATM network: moves cell along VC to destination
at Destination Host:
  AAL5 reassembles cells into original datagram
  if CRC OK, datagram is passed to IP

## Slide 98: IP-Over-ATM
Issues:
IP datagrams into ATM AAL5 PDUs
from IP addresses to ATM addresses
  just like IP addresses to 802.3 MAC addresses!
ATM
network
Ethernet
LANs

## Slide 99: Multiprotocol label switching (MPLS)
initial goal: speed up IP forwarding by using fixed length label (instead of IP address) to do forwarding
  borrowing ideas from Virtual Circuit (VC) approach
  but IP datagram still keeps IP address!
PPP or Ethernet
header
IP header
remainder of link-layer frame
MPLS header
label
Exp
S
TTL
20
3
1
5

## Slide 100: MPLS capable routers
a.k.a. label-switched router
forwards packets to outgoing interface based only on label value (don’t inspect IP address)
  MPLS forwarding table distinct from IP forwarding tables
signaling protocol needed to set up forwarding
  RSVP-TE
  forwarding possible along paths that IP alone would not allow (e.g., source-specific routing) !!
  use MPLS for traffic engineering
must co-exist with IP-only routers

## Slide 101: MPLS forwarding tables
R1
R2
D
R3
R4
R5
0
1
0
0
A
R6
in out out
label label dest interface
6 - A 0
in out out
label label dest interface
10 6 A 1
12 9 D 0
in out out
label label dest interface
10 A 0
12 D 0
1
in out out
label label dest interface
8 6 A 0
0
8 A 1

## Slide 102: Chapter 5: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
instantiation and implementation of various link layer technologies
  Ethernet
  switched LANS
  PPP
  virtualized networks as a link layer: ATM, MPLS

## Slide 103: Chapter 5: let’s take a breath
journey down protocol stack complete (except PHY)
solid understanding of networking principles, practice
….. could stop here …. but lots of interesting topics!
  wireless
  multimedia
  security
  network management